## Slide 1
PROGRESS UPDATE 2
Drunky: Robot Bartender
🍹· 🥃 ·🍸
An automated bartender system built on two SO-101 arms, imitation learning, and color and label based perception.
COURSE
TECHIN 517 — Robotics Final Project
TEAM
Tony Chen · Rushav Dash · Joyce Zhou
INSTITUTION
University of Washington Global Innovation Exchange
DATE
May 2026

## Slide 2
WHERE WE LEFT OFF
Previous progress
Previously completed
Alcohol Bottle Detection and Classification
Collected 100+ images of shooter bottles and fine-tuned YOLO. Localize bottles on the shelf and get pose coordinates
ACT grab policy v1
Imitation learning pipeline validated: teleoperation, data collection, ACT training, and autonomous inference
Dual-arm ROS 2 stack
Synchronized control of both SO-101 arms over a shared topic graph
Environment set-up
Docker environment configured with ROS 2 Humble, LeRobot, and RealSense support
Recently completed
DRUNKY · PROGRESS UPDATE 2
02
Rosetta integration
Deployed the ACT policy through the Rosetta pipeline for ROS 2-based inference
ACT grab policy v2
Policy scoped down to bottle grabbing only; trained on 66 right-arm episodes and 32 left-arm episodes
Classical pose sequence
Pre-recorded poses for pouring, tossing bottle, and pushing the drink forward

## Slide 3
DEMO REEL
System in action
Image
Bottle detection
CLIP_02.MP4 · 1920×1080
Grab + pour policy (right arm)
CLIP_03.MP4 · 1920×1080
Grab policy (left arm)
CLIP_04.MP4 · 1920×1080
Tose/dispose
CLIP_05.MP4 · 1920×1080
Serving
DRUNKY · PROGRESS UPDATE 2
03

## Slide 4
SINCE THE LAST UPDATE
Team contributions
DRUNKY · PROGRESS UPDATE 2
04
Collaborative
Tony Chen
Perception & Policy
Rushav Dash
Data & Rosetta
Joyce Zhou
Data & Forward Kinematics

## Slide 5
PLAN VS. REALITY
Evaluation
Evaluation plan
Pour accuracy
Yes or No
End-to-end task success rate
> 70%
Drink type detection
> 90%
Full cycle time (grab → pour → toss→ serve)
< 180 s
Recovery from a single slip / mis-grasp
retry once
Results so far (right arm grab)
Grabbing success rate average
88.33%
Grabbing success rate (top-left)
10/10
Grabbing success rate (top-middle)
10/10
Grabbing success rate (top-right)
8/10
Grabbing success rate (bottom-left)
9/10
Grabbing success rate (bottom-middle)
9/10
DRUNKY · PROGRESS UPDATE 2
05
Additional side plan
Stir drink before serving
Grabbing success rate (bottom-right)
7/10

## Slide 6
TOWARD FINAL PRESENTATION
Remaining work & final goal
WEEK 7+8
End-to-end integration
Connect all pose sequences with the LeRobot grab policy through Rosetta and begin full pipeline test runs.
WEEK 9
Evaluation spring
Run 10-trial evaluation sets per drink; measure pour accuracy, cycle time, and success rate against targets.
WEEK 10
Final deliverables
Clean up the repo, document the system, and prepare the final presentation and live demo.
FINAL GOAL
Reliably detect, grab, pour, and toss a single drink — closed-loop, with no human intervention — in under 180 seconds , on at least 7 out of 10 consecutive trials.
DRUNKY · PROGRESS UPDATE 2
06

## Slide 7
Thank you.
Questions?
Drunky: Robot Bartender
TONY CHEN · RUSHAV DASH · JOYCE ZHOU
UNIVERSITY OF WASHINGTON GLOBAL INNOVATION EXCHANGE · TECHIN 517